## Slide 1
Mitigating Risks in Compressed Hydrogen Energy Storage
A Quantitative Risk Assessment Approach
November 17, 2025
ENERGY SYSTEMS | NPRE
NPRE 498 - TERM PROJECT
Ami Nicodemus

## Slide 2
Objectives
ENERGY SYSTEMS | NPRE
2
Be familiar with Hydrogen
  Compressed Storage Method using Storage Vessels
  Risks of Hydrogen Storage using Storage Vessels
Risk Analysis on Hydrogen Energy Storage System
  Critically analyze a Research Article
  Supplement its gaps through Quantitative Risk Analysis
  Provide mitigation measure

## Slide 3
Outline of the Presentation
Introduction
Critique of the Research Article
Why Risk Analysis?
QRA Methodology
  What is Hydrogen?
  Why Hydrogen Storage is Important?
  What is Compressed Hydrogen Storage?
  Methodology & Results
  Observations
  Risks Involved in Compressed Storage Vessels
  Why Risk Analysis is Crucial?
  Event Tree / Fault Tree Analysis
  Fussell-Vesely Importance Measure
ENERGY SYSTEMS | NPRE
Impact Assessment
  Key Takeaways
3
Risk Mitigation Strategies
  Synthesis

## Slide 4
ENERGY SYSTEMS | NPRE
4
What is Hydrogen?
  'hydro' and 'genes' meaning water forming
  Most abundant element in the universe
  Lightest of all gases
  High energy density
  Clean-burning Fuel
  Versatile energy
  Fuel cell in Transportation
  Energy Carrier in Power generation
  Industry refining & production processes
Hydrogen as an Element
Hydrogen as a Fuel
Hydrogen as Growing Economy
https://www.rsc.org/periodic-table/element/1/hydrogen
https://ieeexplore.ieee.org/document/9740444
https://www.iea.org/reports/the-future-of-hydrogen
Introduction
ENERGY SYSTEMS | NPRE

## Slide 5
5
ENERGY SYSTEMS | NPRE
Introduction
Why is Hydrogen Storage Important?
  Long period storage for energy produced in surplus months for use during high demand
  Can be converted back to electricity using fuel cells or directly as fuel
Energy Storage & Supply Stability
Seasonal Storage
Flexibility in Energy Systems
  Enables hydrogen to be produced during periods of excess renewable energy generation
Economic Benefits
  Production can take advantage of the low electricity price during off-peak times
Abomazid, A. M., El-Taweel, N. A., & Farag, H. E. Z. (2022). Optimal energy management of hydrogen energy facility using integrated battery energy storage and solar photovoltaic systems. IEEE Transactions on Sustainable Energy, 13(3), 1457-1468.
ENERGY SYSTEMS | NPRE

## Slide 6
4
ENERGY SYSTEMS | NPRE
Introduction
What is Compressed Hydrogen Energy Storage?
  Used in various sectors, including automotive (for fuel cell vehicles), industrial (for chemical processes), and energy storage (to balance intermittent renewable energy sources).
  Engineered to hold hydrogen gas under pressure, allowing for efficient storage and transportation
  Enable the storage of hydrogen in a compact form
  Typically cylindrical with spherical ends, which helps distribute stress evenly and enhances structural integrity
  Designed to withstand high pressures, often ranging from 35 MPa to 82.5 MPa
  Equipped with safety mechanisms such as pressure relief devices, valves, and sensors to monitor pressure and detect leaks
High Storage Density
Scalability
Versatility
Advantages:
Disadvantages & Limitations:
  Cost
  Hydrogen Embrittlement
  Limited volume
  Safety monitoring Challenges
  Design and Development Costs
Elberry, A. M., Thakur, J., Santasalo-Aarnio, A., & Larmi, M. (2021). Large-scale compressed hydrogen storage as part of renewable electricity storage systems. International Journal of Hydrogen Energy, 46(29), 15671–15690. https://doi.org/10.1016/j.ijhydene.2021.02.080
6

## Slide 7
ENERGY SYSTEMS | NPRE
7
Why Risk Analysis?
Risks Involved with Compressed Storage Vessels
  Hydrogen is highly flammable
  Leaks and ruptures poses significant risks of fires and explosions
  Jet fires and vapor cloud explosions are critical hazards
Fire and Explosion Hazard
Lethality
System Design Parameters
Le, S. T., Nguyen, T. N., Linforth, S., & Ngo, T. D. (2023). Safety investigation of hydrogen energy storage systems using quantitative risk assessment. International Journal of Hydrogen Energy, 48(7), 2861–2875. https://doi.org/10.1016/j.ijhydene.2022.10.082
  Jet and flash fires are the primary cause of lethality
  Can result from hydrogen leaks
  Higher storage capacities and pressures are associated with increased risks
  Storage size, mass flow rate, storage pressure, and storage temperature significantly influence the risk profile

## Slide 8
Why Risk Analysis?
ENERGY SYSTEMS | NPRE
8
Why Risk Analysis is Crucial?
  Identify potential hazards associated with hydrogen storage, such as leaks, fires, and explosions
  Assessment of the potential consequences of various failure scenarios
Identification of Hazards & Assessment of Consequences
Informed-Decision Making
Le, S. T., Nguyen, T. N., Linforth, S., & Ngo, T. D. (2023). Safety investigation of hydrogen energy storage systems using quantitative risk assessment. International Journal of Hydrogen Energy, 48(7), 2861–2875. https://doi.org/10.1016/j.ijhydene.2022.10.082
  Data-driven insights that inform decision-making regarding the design, operation, and management of hydrogen storage systems
Cost-Effective & Enhance Safety Culture
  By identifying and mitigating risks early in the design process, organizations can avoid costly accidents and liabilities
  Encourages continuous monitoring and improvement of safety practices
Public Safety & Acceptance
  Ensure public safety and gain community acceptance

## Slide 9
Critique of the Research Article
Le, S. T., Nguyen, T. N., Linforth, S., & Ngo, T. D. (2023). Safety investigation of hydrogen energy storage systems using quantitative risk assessment. International Journal of Hydrogen Energy, 48(7), 2861–2875. https://doi.org/10.1016/j.ijhydene.2022.10.082
Methodology Used for Risk Analysis
Findings are integrated to assess the overall risk associated
Analyzes the likelihood of different hazardous events occurring (Event Tree Analysis)
Assess the potential consequences of identified hazards using Miller model for jet fire hazards and the TNO multi-energy model for explosion hazards
Evaluates the lethal effects of accidental scenarios, including heat radiation and overpressure from explosions
Gathering relevant data and identifying potential hazards associated
Risk Analysis
Frequency Analysis
Consequence Analysis
Impact Assessment
Data Collection & Hazard Identification
ENERGY SYSTEMS | NPRE
9

## Slide 10
Critique of the Research Article
Le, S. T., Nguyen, T. N., Linforth, S., & Ngo, T. D. (2023). Safety investigation of hydrogen energy storage systems using quantitative risk assessment. International Journal of Hydrogen Energy, 48(7), 2861–2875. https://doi.org/10.1016/j.ijhydene.2022.10.082
ENERGY SYSTEMS | NPRE
10

## Slide 11
Critique of the Research Article
Le, S. T., Nguyen, T. N., Linforth, S., & Ngo, T. D. (2023). Safety investigation of hydrogen energy storage systems using quantitative risk assessment. International Journal of Hydrogen Energy, 48(7), 2861–2875. https://doi.org/10.1016/j.ijhydene.2022.10.082
Findings of the Research
  Large storage capacities or high storage pressures could exceed acceptable risk threshold
  1E-6 risk contours result could not be contained within the boundaries of the hydrogen storage system
1
2
3
  Storage capacity and storage pressure, have a significant impact on the risk
  As storage capacity and storage pressure increase, leakage or rupture probability also increase
  Crucial for identifying and effectively mitigating safety risks
Significant Impact
Unacceptable & Needs Mitigation
Need for QRA
Design Parameters
Further Research
Risk Levels
ENERGY SYSTEMS | NPRE
11

## Slide 12
Critique of the Research Article
Le, S. T., Nguyen, T. N., Linforth, S., & Ngo, T. D. (2023). Safety investigation of hydrogen energy storage systems using quantitative risk assessment. International Journal of Hydrogen Energy, 48(7), 2861–2875. https://doi.org/10.1016/j.ijhydene.2022.10.082
Observations
1
Limited Scope of Hazards
2
Presentation of Results
3
Risk Mitigation Discussion
4
Future Research Directions
  Do not address all potential hazards associated (Other factors, such as equipment failure, human error, and external threats (e.g., random accidents)
  Treated the failure probabilities of the system components (like pipes, valves, and joints) and the likelihood of hydrogen leakage as the same thing.
  While individual risk contours are mentioned, visual representations of these contours could enhance understanding.
  More explicit connections between the results and their implications for safety measures would strengthen the research.
  Needs more detailed discussion of specific strategies or technologies that could be implemented to reduce identified risks.
  It could offer more specific recommendations or areas of focus for studies.
ENERGY SYSTEMS | NPRE
12

## Slide 13
QRA Methodology
Methodology Used for Risk Analysis
Findings are integrated to assess the overall risk associated
Analyzes the likelihood of different hazardous events occurring (Event Tree Analysis)
Assess the potential consequences of identified hazards using Miller model for jet fire hazards and the TNO multi-energy model for explosion hazards
Evaluates the lethal effects of accidental scenarios, including heat radiation and overpressure from explosions
Gathering relevant data and identifying potential hazards associated
Risk Analysis
Frequency Analysis
Consequence Analysis
Impact Assessment
Data Collection & Hazard Identification
ENERGY SYSTEMS | NPRE
13

## Slide 14
QRA Methodology
Calculated Risk on Critiqued Research Article
ENERGY SYSTEMS | NPRE
14
Le, S. T., Nguyen, T. N., Linforth, S., & Ngo, T. D. (2023). Safety investigation of hydrogen energy storage systems using quantitative risk assessment. International Journal of Hydrogen Energy, 48(7), 2861–2875. https://doi.org/10.1016/j.ijhydene.2022.10.082

## Slide 15
QRA Methodology
Event Tree Analysis (ETA)
Figure 1. ETA from research article Le et al. 2023
  Do not address all potential hazards associated
  All component and hydrogen leakage failure probabilities are the same
  Pr(Failure) = 1E-6
ENERGY SYSTEMS | NPRE
15
1
Limited Scope of Hazards

## Slide 16
QRA Methodology
Event Tree Analysis (ETA)
Figure 2. Term paper’s ETA based on Zarei et al. (2017)
Zarei et al. (2017), "Dynamic Safety Assessment of Natural Gas Stations Using Bayesian Network," Journal of Hazardous Materials 321: 830 – 840
Accident scenario modeling based on the worst-case scenario and examines the properties and behavior of hydrogen gas during a leakage
ENERGY SYSTEMS | NPRE
16

## Slide 17
QRA Methodology
Fault Tree Analysis (FTA)
Figure 2. Term paper’s ETA based on Zarei et al. (2017)
ENERGY SYSTEMS | NPRE
17

## Slide 18
QRA Methodology
FTA of Hydrogen Leakage as Initiating Event
ENERGY SYSTEMS | NPRE
18
Correa-Jullian, C., & Groth, K. M. (2022). Data requirements for improving the quantitative risk assessment of liquid hydrogen storage systems. International Journal of Hydrogen Energy, 47(6), 4222–4235 [11] and Zarei et al. (2017), "Dynamic Safety Assessment of Natural Gas Stations Using Bayesian Network," Journal of Hazardous Materials 321: 830 – 840.
Figure 3. FTA of Leak Top Event
Table 1. Probability of the Basic Events for Hydrogen Leakage

## Slide 19
QRA Methodology
FTA of Auto Emergency Shutdown Failure as Top Event
ENERGY SYSTEMS | NPRE
19
Zarei et al. (2017), "Dynamic Safety Assessment of Natural Gas Stations Using Bayesian Network," Journal of Hazardous Materials 321: 830 – 840.
Figure 4. FTA of Auto Emergency Shutdown Failure Top Event
Table 2. Probability of the Basic Events for
Auto Emergency Shutdown Failure

## Slide 20
QRA Methodology
FTA of Manual Emergency Shutdown Failure as Top Event
Zarei et al. (2017), "Dynamic Safety Assessment of Natural Gas Stations Using Bayesian Network," Journal of Hazardous Materials 321: 830 – 840.
Figure 5. FTA of Manual Emergency Shutdown Failure Top Event
ENERGY SYSTEMS | NPRE
20
Table 3. Probability of the Basic Events for
Manual Emergency Shutdown Failure

## Slide 21
QRA Methodology
Frequency of Event Tree Failure Scenarios
Zarei et al. (2017), "Dynamic Safety Assessment of Natural Gas Stations Using Bayesian Network," Journal of Hazardous Materials 321: 830 – 840.
ENERGY SYSTEMS | NPRE
21
Table 4. Failure probabilities of Top Events
Failure Scenarios based on ET:

## Slide 22
QRA Methodology
Total Failure Frequency
ENERGY SYSTEMS | NPRE
22
To calculate the total failure frequency, the three scenarios above must be summed:
=
Modarres, M., Kaminskiy, M. P., & Krivtsov, V. (2016). Reliability engineering and risk analysis: A practical guide (3rd ed.). CRC Press

## Slide 23
Impact Assessment
Key Takeaways
ENERGY SYSTEMS | NPRE
24
According to ISO 19880-1:
  Risk for workers inside a facility should not exceed 1E-04 per year
  Risk for third parties outside the facility should not exceed 1E-06 per year
Figure 7. ISO 19880-1 Third Party Risk vs. Computed Risk
ISO. (2020). ISO 19880-1: Gaseous hydrogen – Fueling stations – Part 1: General requirements. International Organization for Standardization

## Slide 24
QRA Methodology
ENERGY SYSTEMS | NPRE
23
Fussell-Vesely Importance Measure
Assess the contribution of each individual cut set to the overall system failure probability where each basic event is varied individually, and the resulting change in system risk is evaluated.
Figure 6. Fussell-Vesely Importance Measure of Basic Events
Modarres, M., Kaminskiy, M. P., & Krivtsov, V. (2016). Reliability engineering and risk analysis: A practical guide (3rd ed.). CRC Press

## Slide 25
Risk Mitigation Strategies
ENERGY SYSTEMS | NPRE
25
Synthesis
ISO. (2020). ISO 19880-1: Gaseous hydrogen – Fueling stations – Appendix B: Further Guidance on Risk Management.
International Organization for Standardization.
Hydrogen Gas Accumulation Mitigation Measures
1. Passive ventilation
2. Active ventilation
3. Hydrogen gas detection system
4. Integrity testing of isolated piping sections
5. Other means of leak detection, such as ultrasonic gas detection
Automatic Emergency Shutdown Failure Mitigation Measures
For Basic Event X37: Tearing of Sleeves
For Basic Event X31: Not Testing of Run along with Sensing
Install pressure relief devices, such as spring-loaded, pressure-actuated safety valves or non-resealable pressure-actuated safety devices
Proper maintenance, regular testing, and reliable sensing

## Slide 26
References
ENERGY SYSTEMS | NPRE
26
[1] Royal Society of Chemistry. (n.d.). Hydrogen – Element information, properties and uses. https://periodic-table.rsc.org/element/1/hydrogen
[2] Rivero, R., Jefferson, K., & … (2022). Optimal energy management of hydrogen energy facility using integrated battery energy storage and solar photovoltaic systems. IEEE Journals & Magazine. https://ieeexplore.ieee.org/document/9740444
[3] International Energy Agency. (2019). The future of hydrogen: Seizing today’s opportunities. https://www.iea.org/reports/the-future-of-hydrogen
[4] Elberry, A. M., Thakur, J., Santasalo-Aarnio, A., & Larmi, M. (2021). Large-scale compressed hydrogen storage as part of renewable electricity storage systems. International Journal of Hydrogen Energy, 46(29), 15671–15690. https://doi.org/10.1016/j.ijhydene.2021.02.080
[5] International Energy Agency. (2019). The future of hydrogen—Analysis. International Energy Agency. https://www.iea.org/reports/the-future-of-hydrogen
[6] Abomazid, A. M., El-Taweel, N. A., & Farag, H. E. Z. (2022). Optimal energy management of hydrogen energy facility using integrated battery energy storage and solar photovoltaic systems. IEEE Transactions on Sustainable Energy, 13(3), 1457–1468. https://doi.org/10.1109/TSTE.2022.3161891
[7] Ananthachar, V., & Duffy, J. J. (2005). Efficiencies of hydrogen storage systems onboard fuel cell vehicles. Solar Energy, 78(5), 687–694. https://doi.org/10.1016/j.solener.2004.02.008
[8] Møller, K. T., Jensen, T. R., Akiba, E., & Li, H. (2017). Hydrogen - A sustainable energy carrier. Progress in Natural Science: Materials International, 27(1), 34–40. https://doi.org/10.1016/j.pnsc.2016.12.014
[9] Bossel, U., & Eliasson, B. (n.d.). Energy and the hydrogen economy. Alternative Fuels Data Center. https://afdc.energy.gov/files/pdfs/hyd_economy_bossel_eliasson.pdf
[10] de Miranda, P. E. V. (Ed.). (2019). Hydrogen storage and transport technologies. In Science and engineering of hydrogen-based energy technologies (pp. 221–228). Academic Press.
[11] Ade, N., Wilhite, B., & Goyette, H. (2020). An integrated approach for safer and economical design of hydrogen refueling stations. International Journal of Hydrogen Energy, 45(56), 32713–32729. https://doi.org/10.1016/j.ijhydene.2020.08.232
[12] Abohamzeh, E., Salehi, F., Sheikholeslami, M., Abbassi, R., & Khan, F. (2021). Review of hydrogen safety during storage, transmission, and applications processes. Journal of Loss Prevention in the Process Industries, 72, 104569. https://doi.org/10.1016/j.jlp.2021.104569
[13] Hadef, H., Negrou, B., González Ayuso, T., Djebabra, M., & Ramadan, M. (2020). Preliminary hazard identification for risk assessment on a complex system for hydrogen production. International Journal of Hydrogen Energy, 45(20), 11855–11865. https://doi.org/10.1016/j.ijhydene.2019.10.162
[14] Correa-Jullian, C., & Groth, K. M. (2022). Data requirements for improving the quantitative risk assessment of liquid hydrogen storage systems. International Journal of Hydrogen Energy, 47(6), 4222–4235. https://doi.org/10.1016/j.ijhydene.2021.10.266
[15] LaChance, Jeffrey L, Houf, William G, Fluer, Inc., Paso Robels, CA, Fluer, Larry, & Middleton, Bobby. Analyses to support development of risk-informed separation distances for hydrogen codes and standards. United States. https://doi.org/10.2172/983689
[16] Zarei et al. (2017), "Dynamic Safety Assessment of Natural Gas Stations Using Bayesian Network," Journal of Hazardous Materials 321: 830 – 840.
[17] Modarres, M., Kaminskiy, M. P., & Krivtsov, V. (2016). Reliability engineering and risk analysis: A practical guide (3rd ed.). CRC Press.
[18] ISO. (2020). ISO 19880-1: Gaseous hydrogen – Fueling stations – Part 1: General requirements. International Organization for Standardization.
[19] ISO. (2020). ISO 19880-1: Gaseous hydrogen – Fueling stations – Appendix B: Further Guidance on Risk Management. International Organization for Standardization.

## Slide 27
Mitigating Risks in Compressed Hydrogen Energy Storage
A Quantitative Risk Assessment Approach
November 17, 2025
ENERGY SYSTEMS | NPRE
NPRE 498 - TERM PROJECT
Ami Nicodemus