## Slide 1
Nuclear Hydrogen Production
Binish Fatima Basathia - MEng Energy Systems

## Slide 2
High-capacity factor
High reliability
High energy density
High specific energy
Clean fuel
The specific energy produced by nuclear fission of U-235 is 79,390,000 MJ/kg
Nuclear Power: The Advantages
  https://www.energy.gov/ne/articles/nuclear-power-most-reliable-energy-source-and-its-not-even-close
  https://whatisnuclear.com/energy-density.html
Fuel type
Specific Energy [MJ/kg]
Coal
Oil
Natural Gas
Lithium
30
42
53.5
43

## Slide 3
(IDEAL)
Not done infinitely slowly
Frictional losses
Other heat losses
REAL Heat Engine
  Higher hot reservoir temperature?
  Boiling of primary coolant!!
  High pressure!!
  Metallurgical limits!
Can we increase efficiency somehow?
Typical condenser temperature: 41.5C = 315K
Typical steam temperature: 275.6C = 549K
Cold reservoir
Hot reservoir
Carnot efficiency for a heat engine:
Super Critical Water Reactors (SCWR)
> 22.1 MPa
  https://www.nuclear-power.com/nuclear-engineering/thermodynamics/laws-of-thermodynamics/thermal-efficiency/thermal-efficiency-of-nuclear-power-plants/

## Slide 4
Nuclear Power Plants: The Challenges
Low Efficiency
No load following
Fuel is expensive
Fuel safety
Shutdown time
Summer load curve for houses in NSW
Winter load curve for houses in NSW
  https://www.solarchoice.net.au/blog/how-do-i-use-electricity-throughout-the-day-the-load-curve/

## Slide 5
The hydrogen economy
Hydrogen fuel-cell based vehicles
Energy storage medium
Energy transmission medium

## Slide 6
Steam
Steam
Electricity
Nuclear reactor
Steam Turbine
High Temperature Electrolyzer cell
Produced Hydrogen
Grid
Potential of Hydrogen and Energy cogeneration at Nuclear Power Plants
  Frick, Konor, et al. "Technoeconomic assessment of hydrogen cogeneration via high temperature steam electrolysis with a light-water reactor." Applied Energy 306 (2022): 118044.
  Kowalczyk, Tomasz, Janusz Badur, and Mateusz Bryk. "Energy and exergy analysis of hydrogen production combined with electric energy generation in a nuclear cogeneration cycle." Energy Conversion and Management 198 (2019): 111805.
Energy production flexibility
Capitalizing Hydrogen Market
Increased power plant efficiency
Around 10% increase in net energy efficiency[2]

## Slide 7
Solid Oxide Electrolysis Cells for High Temperature Electrolysis
Solid Oxide Electrolyte
Steam
Pure
Hydrogen
Operating temperature: 600 - 900C
Oxide ions pass through the membrane
Cathode:
Anode:
  https://www.youtube.com/watch?v=fLm0SA1gfWY
  https://www.youtube.com/watch?v=5XFQeHJHWJY

## Slide 8
Thermal energy provided
Energy breakdown for electrolysis
Energy required for electrolysis
Required Electrical Energy
Entropy change
  Magdi M. Ragheb and Behzad Salimi, “Catalyzed Deuterium-Deuterium and Deuterium?Tritium Fusion Blankets for High Temperature Process Heat Production,” Nuclear Technology/Fusion, Vol. 2, pp. 55-72, Jan. 1982.

## Slide 9
If we could create higher temperatures
Steam
Steam
Electricity
Nuclear reactor
Steam Turbine
High Temperature Electrolyzer cell
Produced Hydrogen
Grid
  Different primary coolant gas
  Heat exchangers for steam
  Materials are expensive??
  High efficiency of electrolysis
  Maybe use waste heat to increase efficiency even more??