## Slide 1: Non-flammable electrolytes for Li-ion Batteries
Dong Ok Kim
NPRE 498 Fall 2023

## Slide 2: Li-ion Batteries
Chem. Rev. 2018, 118, 11433−11456

## Slide 3: Li-ion Batteries
Physical Chemistry Chemical Physics 17, no. 43 (2015): 28441-28450.
Energies 2020, 13(19), 5117

## Slide 4: Conventional Electrolytes
Nature Materials volume 19, pages1006–1011 (2020)
Science350,938-943(2015)
Non-aqueous, carbonate-based organic solvents
Traditional aqueous electrolyte
Pure H2O
Non-aqueous electrolyte
Why non-aqueous?
  Limitation on electrochemical window by oxygen evolution reaction and hydrogen reduction reaction
Molecules 2017, 22(3), 403

## Slide 5: Safety Concerns
Energy Storage Materials 10 (2018) 246–267
Journal of Energy Chemistry 59 (2021) 83–99

## Slide 6: Non-flammable Electrolytes
Flame Retardants
Concentrated Electrolytes
Ionic Liquids
Aqueous Electrolytes

## Slide 7: Flame Retardants
Phosphorous containing organic molecules
Good thermal stability, low toxicity and low volatility
Limitations
  Doesn’t completely remove flammability from electrolytes
  Not compatible with graphite electrode (poor oxidative stability)
Batteries 2019, 5(1), 19

## Slide 8: Flame Retardants
Fluorinated methyl group of a conventional organic molecules
Non-flammable after flame tests
Improvement in the battery performance overall
Limitations
  High viscosity and low ionic conductivity
  Expensive costs
Mater. Horiz., 2021, 8, 2913–2928
Batteries 2019, 5(1), 19

## Slide 9: Highly concentrated electrolytes
Electrolyte with salt concentration higher than 4 M
Volatility and vapor pressure decrease
Significant amount of electrolyte is non-combustible salt
Improves battery performance overall
Limitations
  High viscosity, poor wettability, high costs (due to expensive salt)
NATURE COMMUNICATIONS | 7:12032

## Slide 10: Diluted (localized) High Concentrated Electrolytes
Addition of inert diluent to the electrolyte
  Usually hydrofluoroethers (HFEs)
The diluent itself does not dissolve the salt
Locally forms highly concentrated electrolyte structure
Compared to concentrated electrolyte:
  Less salt needed for the same phenomena (more affordable)
  Less viscous electrolyte
Nature Energy volume 4, pages269–280 (2019)
Adv.Mater.2018, 30, 170610
BTFE
TFEO
Limitations
  HFEs can be flammable as well
  HFEs are fluorinated molecules  environmental and economical issue

## Slide 11: Ionic Liquids (ILs)
Molten salts with melting point (MP) below 100 ºC
  Organic cation + inorganic/organic anion  weak coulombic interaction leading to low MP
Top Curr Chem (Z) (2017) 375:20

## Slide 12: Ionic Liquids
Nonflammable and high thermal stability
Broad electrochemical window and high ionic conductivity
Limitations
  Decomposition products are ignitable gases
  High costs
Electrochimica Acta 148 (2014) 39–45

## Slide 13: Aqueous Electrolytes (Water-in-Salt)
Groundbreaking study in 2015
  Previous Aqueous battery: < 2.0 V
  In 2015, the paper reported 3.0 V Aqueous battery
Science350,938-943(2015)
Traditional aqueous electrolyte
Pure H2O

## Slide 14: Aqueous Electrolytes (Water-in-Salt)
High concentrated aqueous electrolyte
  Electrolyte composition: 20 m LiTFSI in water
  Formation of inorganic-rich, stable electrode-electrolyte interface
  Reduced electrochemical activity of water
Science350,938-943(2015)
Lithium bis(trifluoromethane sulfonyl)imide, LiTFSIç

## Slide 15: Aqueous Electrolytes (Water-in-Salt)
Limitations
  Anode that can be used excludes energy-dens anode materials such as silicon, graphite, and Li metal leading to low capacity
  Hydrogen evolution reaction happens at the anode and disrupts a stable interphase formation
Science350,938-943(2015)
Chem. Soc. Rev., 2021, 50, 10486–10566
Aqueous Electrolyte
Conventional Electrolyte

## Slide 16: Conclusion
Conventional organic electrolytes for lithium-ion batteries involve numerous safety hazards such as thermal runaway
Studies have reported different types of non-flammable electolytes
  Non-flammable additives
  High concentration electrolyte
  Ionic Liquids
  Aqeuous electrolyte
Each method still invovles limitations that need improvement

## Slide 17: Thank you
Any question?