## Slide 1: “Solid-State Batteries”
Department of Nuclear Plasma & Radiological Engineering
NPRE 498: Energy Storage Engineering
Fall 2024
Presented by: Harsh Thakur (hthakur3)
Date: 11/15/2024

## Slide 2: Introduction
Definition: Solid-state batteries (SSBs) are energy storage devices that use a solid electrolyte instead of the conventional liquid electrolyte.
Background: First introduced in the 1990s as an advancement over traditional lithium-ion batteries.
Key Difference: Solid electrolytes improve battery safety and efficiency by eliminating risks associated with liquid electrolytes, such as leakage and flammability.
Applications: Widely used in electric vehicles, portable electronics, and medical devices due to their superior performance and safety.

## Slide 3: Difference between lithium ion and solid-state battery
Accessed from “https://article.murata.com/en-us/article/basic-lithium-ion-battery-4” November(2024)
Fig. Charging and discharging of battery

## Slide 4: Working of Solid-State Battery
Accessed from “https://www.flashbattery.tech/en/how-solid-state-batteries-work/” November(2024)
Fig. structure of sulfide based soil state battery
Cathode - LFP, NMC, LMO.
Anode- Pure lithium
Separator- generally ceramic or polymer

## Slide 5: Examples of SSBs
Accessed from “https://article.murata.com/en-us/article/basic-lithium-ion-battery-4” November(2024)
1. NASICON-type Batteries
Electrolyte: Sodium Super Ionic Conductor (Na₃Zr₂Si₂PO₁₂).
Features: High ionic conductivity and good thermal stability.
Applications: Used in energy storage systems due to their wide electrochemical stability window.

## Slide 6: Examples of SSBs
Accessed from “https://article.murata.com/en-us/article/basic-lithium-ion-battery-4” November(2024)
2. Garnet-type Batteries
Electrolyte: Lithium Lanthanum Zirconium Oxide (LLZO).
Features: High chemical and mechanical stability.
Applications: Commonly used in electric vehicles (EVs) and other high-performance devices.

## Slide 7: Examples of SSBs
Accessed from “https://article.murata.com/en-us/article/basic-lithium-ion-battery-4” November(2024)
3. Sulfide-based Solid-State Batteries
Electrolyte: Lithium Phosphorus Sulfide (Li₁₀GeP₂S₁₂).
Features: Extremely high ionic conductivity and good compatibility with lithium metal anodes.
Applications: Considered for EVs and grid storage.

## Slide 8: Examples of SSBs
Accessed from “https://article.murata.com/en-us/article/basic-lithium-ion-battery-4” November(2024)
4. Perovskite-type Batteries
Electrolyte: Lithium Lanthanum Titanium Oxide (LLTO).
Features: High bulk ionic conductivity but challenges with grain boundary resistance.
Applications: Suitable for applications requiring high power density.
.

## Slide 9: Examples of SSBs
Accessed from “https://article.murata.com/en-us/article/basic-lithium-ion-battery-4” November(2024)
5. LIPON-based Batteries
Electrolyte: Lithium Phosphorus Oxynitride (LIPON).
Features: Thin-film solid electrolyte with good stability and low electronic conductivity.
Applications: Used in microbatteries for medical devices and small electronic devices.

## Slide 10: Solid-State Li-ion Battery Reaction
Reduction (cathode):
Oxidation (anode):
Full reaction:+ +
Notten, P. H. L., & Danilov, D. L. (2014). Battery modeling: a versatile tool to design advanced battery management systems. Advances in Chemical Engineering and Science, 04(01), 62–72. https://doi.org/10.4236/aces.2014.41009

## Slide 11: Advantages of SSEs
Safety: Non-flammable and thermally stable.
Performance: Higher energy density and minimal self-discharge.
Durability: Longer life cycles due to reduced dendrite formation.
Fig. shows overview of the evolution of battery technology.
Wang, C., & Sun, X. (2022). The promise of Solid-State batteries for safe and reliable energy storage. Engineering, 21, 32–35. https://doi.org/10.1016/j.eng.2022.10.008

## Slide 12: Ionic conductivity and Temperature
It is ability is to conduct electricity through the movement of ions.
Measuring unit: siemens per meter (S/m)
High ionic conductivity (10− 1 to 10− 4 S/cm)
Low electronic conductivity (< 10− 6 Scm)
Low activation energy (Ea < 0.3 eV)
Aniya, M. (2019). Bonding character and ionic conduction in solid electrolytes. Pure and Applied Chemistry, 91(11), 1797–1806. https://doi.org/10.1515/pac-2018-1220

## Slide 13: Vogel-Tamman-Fulcher equation
= ionic conductivity (S/cm)
= Activation energy of material (J/K mol)
= Arreheinus Factor
R = Gas constant (8.314 J/K mol)
T = Temperature (K)
Perrier, M., Besner, S., Paquette, C., Vallée, A., Lascaud, S., & Prud’homme, J. (1995). Mixed-alkali effect and short-range interactions in amorphous poly(ethylene oxide) electrolytes. Electrochimica Acta, 40(13–14), 2123–2129. https://doi.org/10.1016/0013-4686(95)00151-4

## Slide 14: MATLAB program
Relationship between temperature and ionic conductivity

## Slide 15: Result
Solid state electrolyte (sulfide based)
Ionic conductivity increases with temperature
Fig. Generated through MATLAB

## Slide 16: Conclusion
1. Automotive Industry:
Seen as the future of electric vehicles (EVs) due to higher energy density.
2. Transportation Sector:
Suitable for heavy vehicles (trucks, buses, etc.) that require long range and high energy.
3. Future of Industrial Electrification:
If solid-state batteries become cost-competitive, they could revolutionize industrial applications by improving energy efficiency and reducing reliance on fossil fuels.