## Slide 1: NUCLEAR HYDROGEN PRODUCTION
Clean, Large-Scale H₂ for the Energy Transition
Name- Raj Mohite

## Slide 2
Current Energy Trends: The Push Towards Decarbonization
Global hydrogen demand today: ~70–115 Mt/year (mostly for ammonia, refining, methanol)
Current production dominated by low-cost fossil routes (natural gas + coal)
96% produced from fossil fuels → ~830 Mt CO₂/year
Gray hydrogen (SMR + coal gasification): 10–19 t CO₂ per t H₂
Clean hydrogen (<1 kg CO₂/kg H₂) is <1% of total production
Energy transition requires massive decarbonization of hard-to-abate sectors (steel, cement, heavy transport, chemicals)
Fig 1. Hydrogen production by technology and by region

## Slide 3
Hydrogen Demand to Reach Net-Zero 2050: A Critical Component
Hydrogen demand is projected to grow 5–7 times by 2050, according to the Hydrogen Council and IEA, becoming a cornerstone of the energy transition.
Clean hydrogen must supply a significant portion—20–25%—of final energy in net-zero scenarios.
Achieving this requires approximately 220 Mt/year of zero- or low-carbon hydrogen production by 2050.
Nuclear power, alongside renewables, stands as one of the few scalable and dispatchable low-carbon sources capable of meeting this immense demand.
Fig 2. Global hydrogen demand

## Slide 4: Hydrogen Production Routes – Overview (Color Wheel)
Fig.3 Hydrogen color wheel

## Slide 5: Why Nuclear Hydrogen is Beneficial
Zero operational CO₂ emissions
High capacity factor (>90%) → stable, predictable production (vs intermittent renewables)
Uses both electricity and high-temperature heat (cogeneration) → higher overall efficiency
Large-scale centralized production → lowest distribution costs
Existing nuclear fleet can start immediately using off-peak power
Advanced reactors (SMRs, HTGRs) ideally suited for dedicated hydrogen plants
Enhances grid stability when coupled with electrolyzers
Fig 4. Non-Carbon Nuclear Hydrogen Production Technologies

## Slide 6: Nuclear Hydrogen Production Technologies
1. Low-Temperature Electrolysis (current reactors)
  PEM, AEM
  Uses electricity only (LWRs, SMRs)
  Proven, commercially available
Core Principle- Uses electricity only to split liquid water into H₂ and O₂ at 50–100 °C.
Fig. 5 Nine Mile Point Nuclear Power Station (Oswego, New York)
Fig. 6 Davis-Besse Nuclear Power Station
Fig. 7 Low temperature electrolysis using PEM and AEM

## Slide 7: Nuclear Hydrogen Production Technologies
2. High-Temperature Steam Electrolysis (HTSE)
  Operates at 700–900 °C → ~30–40% less electricity needed
  Needs high-temperature heat source (HTGR, VHTR, advanced SMRs)
Core Principle
HTSE is still electrolysis (splitting water with electricity), but instead of feeding liquid water at 60–100 °C (like normal PEM or Alkaline electrolyzers), you feed superheated steam at 700–900 °C. At these high temperatures, thermodynamics dramatically reduces the electricity needed.
Fig. 9 Prairie Island Nuclear Generating Plant (Red Wing, Minnesota)
Fig. 8 High temperature steam electrolysis
Total energy for splitting water = ΔH (enthalpy) ΔH = Electrical energy (ΔG) + Thermal energy (TΔS) As temperature increases → ΔG decreases (Gibbs free energy) Therefore, less electrical energy is needed

## Slide 8: Nuclear Hydrogen Production Technologies
3. Thermochemical Cycles (e.g., Sulfur-Iodine)
  Purely thermal water splitting at 800–1000 °C
  Highest theoretical efficiency (>50%)
  Still R&D/demonstration stage
Core principle
Thermochemical cycles split water into H₂ and O₂ using only high-temperature heat (no electricity or very little). They work like a chemical “heat engine” that uses heat from a nuclear reactor (800–1000 °C) to drive a closed loop of reactions. At the end of the loop, the chemicals are fully regenerated and the only net outputs are hydrogen and oxygen.
Three main reactions (closed loop):
H₂SO₄ → SO₂ + H₂O + ½ O₂ (850–900 °C) Sulfuric acid decomposes
and releases oxygen
I₂ + SO₂ + 2 H₂O → 2 HI + H₂SO₄ (120 °C) Bunsen reaction (exothermic)
2 HI → I₂ + H₂ (400–500 °C) Hydrogen iodide
decomposes → hydrogen is released
Net result: H₂O → H₂ + ½ O₂
All chemicals (I₂, H₂SO₄, HI, SO₂) are recycled → nothing is consumed except water and heat.
Fig. 10 Sulfur-Iodine thermochemical cycle

## Slide 9: How do the three processes compare with each other?
Feature | Low-Temp Electrolysis | HTSE (High-Temp Electrolysis) | Thermochemical Cycles
Main input | Electricity only | Electricity + heat | Heat only (or tiny electricity)
Operating temperature | 60–100 °C | 700–900 °C | 800–1000 °C
Electricity needed | 50–60 kWh/kg H₂ (Source) | 32–40 kWh/kg H₂ (Source) | 0–5 kWh/kg H₂
Theoretical efficiency | ~70% | ~90–95% | >50% (realistic 45–55%)
Best reactor match | Any nuclear plant | HTGR, MSR | VHTR, Gen-IV HTGR
Maturity (2025) | Commercial | Demonstration | Lab → large demo

## Slide 10: Challenges
Process | #1 Challenge | #2 Challenge
Low-temp Electrolysis | High electricity consumption (50–60 kWh/kg) → expensive H₂ unless using very cheap off-peak nuclear power (Source) | Limited heat integration
HTSE (SOEC) | SOEC materials corrosion & degradation at 700–900 °C (chromium volatilization, electrode delamination) | High stack system cost (Around $1235/kW) (Source)
S-I Thermochemical | Materials corrosion (HI/H₂SO₄) | Chemical separation complexity
All processes | Nuclear-chemical safety licensing | Hydrogen infrastructure gap

## Slide 11: Future Pathways (Beyond Electrolysis & Thermochemical)
Radiolysis: Direct water splitting using gamma radiation (research stage)
Photo-electrochemical + nuclear heat/electricity hybrids
Fusion-neutron-driven hydrogen production (long-term)
Direct use of spent fuel heat for thermochemical cycles (conceptual)
Nuclear-driven methane pyrolysis (turquoise hydrogen)

## Slide 12: Conclusion
Nuclear-Powered Hydrogen: The Missing Scale for Net-Zero 2050
Clean hydrogen is essential to decarbonise steel, ammonia, shipping, aviation and heavy industry
Only nuclear delivers firm, high-capacity-factor, zero-carbon energy at the scale needed (hundreds of Mt/year)
Timeline to commercial reality
  Today → 2030: Low-temperature electrolysis using existing reactors (already operating in the USA)
  2030–2040: HTSE + SMRs/HTGRs → 30–40 % lower electricity demand
  2040+: Thermochemical cycles → lowest-cost clean hydrogen on the planet
Final message Nuclear hydrogen is not a competitor to green hydrogen, it is the indispensable complement that provides the volume, reliability and affordability the world actually needs.

## Slide 13: Sources
1. Author(s). (2025). Title of article. Journal Name, Volume(Issue), pages. https://doi.org/10.1007/s44373-025-00043-9 (Ghezel-Ayagh, A., & co-authors. (2024). Title of paper. U.S. Department of Energy. Retrieved from https://www.hydrogen.energy.gov/docs/hydrogenprogramlibraries/pdfs/review24/ta039_ghezel-ayagh_2024_o.pdf?sfvrsn=af10c194_3
2. International Energy Agency. (2025). Global Hydrogen Review 2025. Retrieved from https://iea.blob.core.windows.net/assets/12d92ecc-e960-40f3-aff5-b2de6690ab6b/GlobalHydrogenReview2025.pdf
3. Author(s). (2020). Title of article. Journal Name, Volume(Issue), pages. https://doi.org/10.1016/S0016-2361(20)32321-8 U.S. Department of Energy. (2022, March). HTE workshop — Strategic analysis. Retrieved from https://www.energy.gov/sites/default/files/2022-03/HTE%20Workshop-Strategic%20Analysis.pdf
4. International Atomic Energy Agency. (n.d.). Nuclear hydrogen production. Retrieved from https://www.iaea.org/topics/non-electric-applications/nuclear-hydrogen-production
5. U.S. Department of Energy. (n.d.). 3 nuclear power plants gearing clean hydrogen production. Retrieved from https://www.energy.gov/ne/articles/3-nuclear-power-plants-gearing-clean-hydrogen-production
6. Bender, M. (2018). HydroGEN: Low-Temperature Electrolysis. U.S. Department of Energy. Retrieved from https://www.hydrogen.energy.gov/docs/hydrogenprogramlibraries/pdfs/review18/pd148_bender_2018_o.pdf?Status=Master
7. SWZ Maritime. (2022, June 15). Hydrogen at risk of being the great missed opportunity of the energy transition! SWZ Maritime. Retrieved from https://swzmaritime.nl/news/2022/06/15/hydrogen-at-risk-of-being-the-great-missed-opportunity-of-the-energy-transition/
8. MHI Spectra. (n.d.). The colors of hydrogen: Expanding ways of decarbonization. Retrieved from https://spectra.mhi.com/the-colors-of-hydrogen-expanding-ways-of-decarbonization
9. Author(s). (2020). Title of article. Journal Name, Volume(Issue), pages. https://doi.org/10.1016/S0360-3199(20)33319-X